# jTechDig documentation
The transformation rules for zooming panning and capturing data point coordinates are summarized below. Basically there are three reference frames.
Parameters of the original picture file	The frame parameters on the main window	The real dimensions in a frame
w_o , h_o are the width and height of the original picture in pixels / (x_Mo, y_Mo) the coordinates of the mouse pointer in the original picture in pixels / (x_Zo, y_Zo) top left point of the zoom window in the reference frame of the original picture / w_Zo , h_Zo the width and height of the zoom window	The picture is aligned to the center of the frame. The v_Gap , h_Gap denote the vertical and horizontal gaps around the picture. / w_f , h_f are the frame size in pixels (jLabel icon size) / (x_Mf, y_Mf) the coordinates of the mouse pointer in the frame in pixels / (x_Zf, y_Zf) top left point of the zoom window in the frame / w_Zf , h_Zf the width and height of the zoom window these are not same as w_Zo , h_Zo because the picture is scaled to be displayed in the available frame size	w_r , h_r are real size (width and height) of the picture in pixels / (x_Mr, y_Mr) the coordinates of the mouse pointer in the real picture frame in pixels / (x_Zr, y_Zr) top left point of the zoom window in the real picture frame / w_Zr , h_Zr the width and height of the zoom window

The mouse location is available through the MouseListener, evt.getX() and evt.getY() and these are valid in the frame (x_Mf, y_Mf) . The mouse functions are
- left mouse click → capture coordinate, (coordinates of the captured points are stored in the reference frame of the original picture in pixels)
- right mouse click → pan,
- mouse wheel → zoom.
w_r w_f The zooming factor is a number greater than one, which denotes the amount of zooming for one mouse wheel “click”. The zooming factor can be derived as k= w_o over w_Zo = h_o over h_Zo = w_r over w_Zf = h_r over h_Zf and w_Zf = w_Zr and h_Zf = h_Zr . The zooming is always maintaining the original aspect ratio and magnifies the area around the mouse pointer.

## h_f Calculating the original coordinates when the displayed figure is zoomed
v_Gap

Pixel coordinates in the
original figure
xMo = xMr*wo/wr;
yMo = yMr*ho/hr;
Pixel coordinates in the scaled
(but not zoomed) figure
xMr = (xMf-vGap)*wr/wZf;
yMr = (yMf-hGap)*hr/hZf;

Clicking the mouse in
the frame over
the zoomed figure
xMf = evt.getX();
yMf = evt.getY();